## Slide 1
Wei Bai
Microsoft Research Asia
Congestion Control Mechanisms
for Data Center Networks

## Slide 2
Google’s worldwide DC map
Microsoft’s DC in Dublin, Ireland
Facebook DC interior
Global Microsoft Azure DC Footprint
Data Centers Around the World
Notes: As we know, many big companies, such as Google, Facebook and Microsoft, have built a lot of data centers around the world to provide services to global users.

## Slide 3
Fabric
INTERNET
Data Center Network (DCN)
Notes: Inside the data center, the hundreds of thousands of servers are connected by this network, data center network, DCN.

## Slide 4: Data center applications really care about latency!
Notes: But unfortunately, applications in data centers really care about latency.

## Slide 5
Revenue decreased by 1% of sales for every 100ms latency
[Speed matters; Greg Linden]
100ms slowdown reduced
# searches by 0.2-0.4%
[Speed matters for Google Web Search; Jake Brutlag]
400ms slowdown resulted
in a traffic decrease of 9%
[Yslow 2.0; Stoyan Stefanov]
Notes: Google, Amazon and Yahoo report that the slowdown of latency seriously degrade user experience and operator revenue.

## Slide 6: Goal of My Research
Low Latency Data Center Networks
Notes: Therefore, the goal of my thesis is to achieve low latency in data center networks.

## Slide 7: Sources of Network Latency
Queueing delay
  Moderate queueing is necessary for high throughput
  Excessive queueing only degrades latency
Retransmission delay
  Fast retransmission: 1 RTT (100s of us)
  Timeout retransmission: several ms

## Slide 8: My Research Work
To reduce queueing delay
  PIAS [NSDI’15] minimizes flow completion time without prior knowledge of flow size info
To reduce retransmission delay
  TLT (ongoing) eliminates congestion timeouts

## Slide 9: PIAS
Joint work with Li Chen, Kai Chen,
Dongsu Han, Chen Tian and Hao Wang

## Slide 10: Flow Completion Time (FCT) is Key
Data center applications
  Desire low latency for short messages
  App performance & user experience
Goal of DCN transport: minimize FCT
  Many flow scheduling proposals
Notes: Many data center applications, such as Web search, machine learning, database and cache, desire ultra low latency for these short messages. The reason is that the completion times of these short messages directly determine the user experience. Therefore, to improve the application performance, one of the most important design goal for data center transport is to minimize flow completion times, especially for short flows. To address this challenge, there are many flow scheduling proposals, [click]

## Slide 11: Existing Solutions
PDQ
SIGCOMM’12
pFabric
SIGCOMM’13
PASE
SIGCOMM’14
All assume prior knowledge of flow size information to approximate ideal preemptive Shortest Job First (SJF) with customized network elements
Not feasible for many applications
Hard to deploy in practice
Notes: Such as PDQ, pFabric and PASE. These solutions can potentially provide very good, even near-optimal performance. However, we find that, [click] all of them assume prior knowledge of flow size information to approximate ideal preemptive shortest job first scheduling. In addition to this, all of these solutions leverage customized network elements. For example, pFabric introduces non-trivial modifications to switch hardware and PASE requires an separate and complex control plane for arbitration. [click] We note that, the assumption of prior knowledge of flow size information does not hold for many cases. For many applications, such as database query and response, data is transferred as soon as it is generated without buffering. So we can not get flow size information beforehand. [click] And the customized network elements make these solutions very hard to deploy in production data centers. So we take one step back [click]

## Slide 12: Question
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
Notes: And ask a fundamental question ……………….. This question transfers to three concrete design goals.

## Slide 13: Design Goal 1
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
Information-agnostic: not assume a priori knowledge of flow size information available from the applications

## Slide 14: Design Goal 2
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
  FCT minimization: minimize the average and tail FCTs of short flows & not adversely affect FCTs of large flows

## Slide 15: Design Goal 3
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
  Readily-deployable: work with existing commodity switches & be compatible with legacy network stacks

## Slide 16: Our Answer
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
PIAS: Practical Information-Agnostic flow Scheduling

## Slide 17: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
Priority 1
Priority 2
Priority K
……
High
Low
Notes: The design rationale of PIAS is performing multi-level feedback queue to emulate shortest job first. As we can see, there are K priority queues in MLFQ. 1 is the highest priority while K is the lowest one. During a flow’s life time, its priority is gradually reduced. [click]

## Slide 18: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
Priority 1
Priority 2
Priority K
……
Notes: For example, for this flow. The first packet is assigned to the priority 1. [click]. The second packet is demoted to priority 2. [click] For the third packet, its priority is further reduced. [click]. Eventually, if this flow is large enough, the last packet is assigned to the lowest priority. You can see that, the key idea of multi-level feedback queue is very simple and it does not require flow size information to do the scheduling.

## Slide 19: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
In general, PIAS short flows finish in higher priority queues while large ones in lower priority queues, emulating SJF, effective for heavy tailed DCN traffic.
Notes: With MLFQ, small flows are more likely to finish in higher priority queues while large flows are more likely to finish in lower priority queues. Therefore, small flows are prioritized over large flows, thus emulating SJF, especially for heavy tailed DCN workloads.

## Slide 20: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
Requires switch to keep per-flow state
Implementing MLFQ at switch directly not scalable
Notes: However, MLFQ is not supported on commodity switches because it’s hard to track per-flow state on switches.

## Slide 21: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
Decoupling MLFQ
  Stateless Priority Queueing at the switch (a built-in function)
  Stateful Packet Tagging at end hosts (a shim layer between TCP/IP and NIC)
- priorities:
thresholds:
- Threshold from to is:
priorities:
thresholds:
Threshold from to is:
priorities:
thresholds:
Threshold from to is:
Notes: To solve this problem, we decouple multi-level feedback queue. On the switch, we enable strict priority queueing [click]. At end hosts, we have a packet tagging module[click]. The logic of packet tagging module is quite simple. Assuming that they are K priorities and K-1 demotion thresholds correspondingly. Note that the P1 is the highest priority. The packet tagging module just maintains per-flow state and compare the bytes sent information with demotion thresholds. If a flow’s bytes sent value is exactly larger than Alpha[j-1], the following packet of this flow will be marked with Pj. For example, [click]

## Slide 22: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
- priorities:
thresholds:
- Threshold from to is:
priorities:
thresholds:
Threshold from to is:
priorities:
thresholds:
Threshold from to is:
i
Decoupling MLFQ
  Stateless Priority Queueing at the switch (a built-in function)
  Stateful Packet Tagging at end hosts (a shim layer between TCP/IP and NIC)
Notes: 解释例子

## Slide 23: Threshold vs Traffic Mismatch
DCN traffic is highly dynamic
  Threshold fails to catch traffic variation → mismatch
High
Low
10MB
10MB
20KB
Ideal, threshold = 20KB
Too small, 10KB
Too big, 1MB
ECN
Notes: To determine demotion thresholds for MLFQ, we build a simple queueing theory model to analyze it and derive demotion thresholds based on flow size distributions. However, traffic is highly dynamic in data centers (across both time and space), so the mismatch between traffic and demotion thresholds is unavoidable. We need to handle the mismatch problem in order keep PIAS effective in highly dynamic data center networks? [click] 解释例子

## Slide 24: PIAS in 1 Slide
PIAS packet tagging
  Maintain flow states and mark packets with priority
PIAS switch
  Enable strict priority queueing and ECN
PIAS rate control
  Employ Data Center TCP to react to ECN

## Slide 25: Prototyping & Evaluation
Prototype implementation
  http://sing.cse.ust.hk/projects/PIAS
Testbed experiments and ns-2 simulations
  1G in testbed experiments
  10G/40G in simulations
  Realistic production traffic
Schemes compared
  DCTCP (both testbed and simulation)
  pFabric (only simulation)
Notes: Now, we come to evaluation part. We have already implemented a PIAS prototype. [click] It is open source. In our implementation, the packet tagging module works as a Linux kernel module, which can be installed and removed during the running time of the system. We use 16 servers and 1 Gigabit switch for our evaluation. For the benchmarks, we use web search workload from DCTCP paper, data mining workload from VL2 paper.

## Slide 26: Testbed: Small Flows (<100KB)
Data Mining
PIAS reduces average FCT of small flows by up to 49% and 34%, compared to DCTCP.
34%
49%
Web Search
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 0.591 | 0.662 | 0.767 | 0.93
DCTCP | 0.83 | 1.004 | 1.261 | 1.824
TCP | 2.515 | 3.251 | 5.042 | 7.29
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 0.281 | 0.282 | 0.283 | 0.285
DCTCP | 0.343 | 0.366 | 0.394 | 0.435
TCP | 2.664 | 3.721 | 5.089 | 6.298
Notes: These two figures show the average completion times of small flows. Compared to DCTCP, PIAS reduces average FCT of small flows by up to 49% in web search workload and 34% in data mining workload. Even though DCTCP try to reduce buffer occupation to achieve low latency, it still needs moderate buffer occupation to fully utilize link capacity. But with PIAS, we can provide much fewer or even zero queueing delay for packets of short flows because they are finished in higher priority queues.

## Slide 27: NS-2: Comparison with pFabric
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 89.2348 | 89.6678 | 90.0634 | 90.359
pFabric | 88.7644 | 89.0419 | 89.2783 | 89.4752
PIAS only has a 1% performance gap to pFabric for small flows in the data mining workload.
Web Search
Data Mining
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 126.0101 | 128.2321 | 132.3223 | 135.5542
pFabric | 114.633 | 115.9524 | 117.3958 | 119.023
Notes: We also compare PIAS against pFabric. Note that pFabric is a information-aware clean-slate design. It assumes prior knowledge of flow size information and introduces changes to switch hardware. For PIAS, we don’t make such assumptions and just use commodity switches. Compared to pFabric, PIAS achieves comparable performance in small flows, especially in data mining workload. [click] The performance gap here here is only 1%.

## Slide 28: PIAS Recap
PIAS: practical and effective
  Not assume flow information from applications
  Enforce Multi-Level Feedback Queue scheduling
  Use commodity switches & legacy network stacks
Information-agnostic
FCT minimization
Readily deployable
Notes: Finally, we conclude our work. We think that PIAS is a practical and effective solution for data centers. First of all, it is information-agnostic without assuming that flow size information available from applications. Secondly, PIAS performs multi-level feedback queue to emulate shortest job fist, thus achieving FCT minimization. Thirdly, PIAS is readily deployable in commodity data centers. It just uses basic functionalities from commodity switches and is compatible with legacy network stacks.

## Slide 29: TLT
Ongoing work with Yibo Zhu, Dongsu Han, Byungkwon Choi, Hwijoon Lim

## Slide 30: Lossy & Loss-Less
Lossy Ethernet
  Packet losses increase end-to-end latency
Loss-Less Ethernet
  Use PFC to eliminate congestion packet losses
  Cause new problems: HoL blocking, deadlock
Can we get benefits from both sides?

## Slide 31: Revisit the Impact of Packet Losses
Packet losses in the middle
  Fast retransmissions: 1 RTT (100s of us)
Packet losses at the tail
  Timeout retransmissions: several ms
1
2
3
ACK1
ACK1
2
1
3
ACK1
ACK2
2
3

## Slide 32: Design Goals
Eliminate timeout retransmissions
Small side effects -> Rarely/Never trigger PFC
Work with commodity switch hardware
Timeout-Less Transport (TLT)

## Slide 33: Design Rationale
Some packets are important as their losses may cause timeouts
  For example, last data packet in a message
Only guarantee important packets lossless
  Unimportant packets can be dropped as usual

## Slide 34: Design Challenges
How to select important packets?
  As few as possible
  For both rate/window protocols
How to guarantee important packets lossless?
  Separating important and unimportant packets into two queues causes out-of-order problem

## Slide 35: Important Packets of Rate Protocols
Last packet of the message must be important
One of every N packets is selected as the important one
  Further reduce retransmission delay

## Slide 36: Important Packets of Window Protocols
Insight: at least one in-flight packet is important
In the first window, randomly choose one important packet
When receiving an ACK for an important packet
  If the window allows, transmit a new packet (or a lost packet) and mark it as important
  Otherwise, transmit the last unacknowledged packet and mark it as important

## Slide 37: Guarantee Important Packets Lossless
Drop thresh.
Important
Unimportant
Switch proactively drops unimportant packets

## Slide 38: Guarantee Important Packets Lossless
Switch proactively drops unimportant packets
  Leave buffer headroom for important packets
  Avoid triggering PFC
Enable PFC to handle extreme cases
  For example, a large # of single-packet flows

## Slide 39: Ongoing & Future Work
Further reduce the size of important traffic
How to choose the dropping threshold for unimportant packets
Interaction with congestion control algorithms
Prototype implementation and evaluation

## Slide 40: Summary
PIAS uses MLFQ to reduce the queueing delay (completion time) for small flows
TLT ensures that every congestion loss can be recovered using fast retransmission

## Slide 41: Thank You!